## Slide 1
A Unified Bayesian Framework for Jointly Inferring System Order
and Parameters of LTI State-Space Models
Hongru Liu
School of Power and Energy
2025/11

## Slide 2
CONTENTS
Background
Methodology
Results
Discussion
Conclusion
SGWRC 2025

## Slide 3
Background
The First Section

## Slide 4
Background
Methodology
Discussion
Conclusion
Results
For all model-based control algorithms, like Pole Placement, LQR, MPC…, the explicit form of f must be known to determine control input.
If the model is difficult to established, like rockets, airplanes, jet engines.
One way is to identify the model’s transfer function or state-space representation.

## Slide 5
Background
Methodology
Discussion
Conclusion
Results
In a Bayesian perspective, parameters are treated as random variables. We infer their posterior probability distribution by combining the likelihood function with a prior distribution.
A state-space representation with unknown parameters A, B, C, D
Bayesian Inference
An estimate state-space representation

## Slide 6
Background
Methodology
Discussion
Conclusion
Results
Current parameters to infer are:
Canonical form
Bryutkin, Andrey, et al. "Canonical bayesian linear system identification." (2025)
The order of system is often unknown.
While the prior uses lambda, it‘s A that is actually inferred, whose physical meaning is not obvious.
Blue: complex eigenvalues
Red: real eigenvalues
We used an RJ-MCMC framework to infer model order and model parameters at the same time. By performing a random walk directly on the ratio of real to complex roots, real and complex roots are identified separately.

## Slide 7
Methodology
The Second Section

## Slide 8
Conclusion
Methodology
Discussion
Results
Background
The detailed balance condition for a standard MCMC algorithm is defined on a fixed-measure space. It compares the transition densities between two points without involving a change of coordinates or a transformation of the underlying measure.
The detailed balance condition implies that the probability flux from state x to state x' equals the probability flux from x' to x.
An Intuitive Grasp of Probability Transition

## Slide 9
Conclusion
Methodology
Discussion
Results
Background
RJ-MCMC uses auxiliary variables to achieve "dimension matching" for moves between spaces. Since this mapping distorts the underlying measure the detailed balance must be corrected, ultimately introducing a Jacobian determinant into the acceptance rate.
The Jacobian term ensures the equality of probability flux in the detailed balance condition !

## Slide 10
Conclusion
Methodology
Discussion
Results
Background
Birth
Death

## Slide 11
Conclusion
Methodology
Discussion
Results
Background
Split
Merge

## Slide 12
Conclusion
Methodology
Discussion
Results
Background
Five categories of random walks:
In the early stages of training, mainly focus on birth-death processes to infer the model order.
In the middle stages of training, mainly focus on split-merge processes to infer the root types.
In the final stages of training, mainly focus on random walking processes to infer the root locations.

## Slide 13
Conclusion
Methodology
Discussion
Results
Background
After the Kalman Filter Process:
At each time step:
The likelihood of the joint distribution over the complete simulation interval:

## Slide 14
Results
The Third Section

## Slide 15
Background
Methodology
Discussion
Conclusion
Results
Birth of real eigen values:
Birth of complex eigen values:
Death of real eigen values:
Death of complex eigen values:
Complex Pair !
Real !

## Slide 16
Background
Methodology
Discussion
Conclusion
Results
Merge of real eigen values:
Split of complex eigen values:
Complex Pair !
Real !
Random swim:
Real !
Complex Pair !

## Slide 17
Background
Methodology
Discussion
Conclusion
Results
Para | Prior(Re) | Prior(Im) | Result(Re) | CV(Re) | Result(Im) | CV(Im)
 | uniform | uniform | 0.52 | 2.1% | / | /
 | uniform | uniform | 0.63 | 0.4% | +0.52i | 0.72%
 | uniform | uniform | 0.63-0.52i | 0.4% | -0.52i | 0.72%
 | N~(0.1,0.2) | / | 0.1200 | 3.61% | / | /
 | N~(0.15,0.2) | / | 0.1500 | 5.26% | / | /
 | N~(0.2,0.2) | / | 0.1999 | 6.74% | / | /

## Slide 18
Discussion
The Forth Section

## Slide 19
Background
Methodology
Discussion
Conclusion
Results
Analysis of the convergence process
After the burn-in process, the model order remains at 3, and its eigenvalues consist of one complex conjugate pair and one real value.
The system order converge because of the convergence of parameters, which is not as expected.

## Slide 20
Background
Methodology
Discussion
Conclusion
Results
Bayesian information criterion
To determine whether to proceed with model order changes a BIC criterion is used:
The posterior of model order and parameter can be applied:
The acceptance ratio then can be determined:

## Slide 21
The Forth Section
Conclusion

## Slide 22
Background
Methodology
Discussion
Conclusion
Results
This work presents a unified identification framework based on the Reversible-Jump Markov Chain Monte Carlo (RJ-MCMC) algorithm for the joint estimation of system order and parameters in state-space models. The key contributions are threefold:
Joint Bayesian Inference: Our method provides a principled Bayesian solution to the challenging problem of simultaneously inferring the model dimension and its parameters, overcoming the limitations of traditional two-step approaches.
Reversible Model Transition: To facilitate flexible exploration of the model space, we designed five specialized moves that allow for the birth, death, and transformation of system poles, all while maintaining the detailed balance condition for valid sampling.
Automatic Order Control: The Bayesian Information Criterion is integrated into the MCMC acceptance ratio. This mechanism automatically penalizes unnecessary complexity, effectively preventing overfitting by controlling the system order.